III. SONAR

Sonar (Sound Navigation and Ranging) is a technique that uses sound propagation (usually underwater, as in submarine navigation) to navigate, communicate with or detect objects on or under the surface of the water, such as other vessels. Two types of technology share the name “sonar”: passive sonar is essentially listening for the sound made by vessels; active sonar is emitting pulses of sounds and listening for echoes. Sonar may be used as a means of acoustic location and of measurement of the echo characteristics of “targets” in the water. Acoustic location in air was used before the introduction of radar. Sonar may also be used in air for robot navigation, and SODAR (upward looking in-air sonar) is used for atmospheric investigations.

The term sonar is also used for the equipment used to generate and receive the sound. The acoustic frequencies used in sonar systems vary from very low (infrasonic) to extremely high (ultrasonic). The study of underwater sound is known as underwater acoustics or hydro acoustics.

i. Sonar Sensing

Sonar or ultrasonic sensing uses propagation of acoustic energy at higher frequencies than normal hearing to extract information from the environment. Sonar is a popular sensor in robotics that employs acoustic pulses and their echoes to measure range to an object. Since the sound speed is usually known, the object range is proportional to the echo travel time. At ultrasonic frequencies the sonar energy is concentrated in a beam, providing directional information in addition to range.

Its popularity is due to its inexpensive cost, light weight, low power consumption, and low computational effort, compared to other ranging sensors. In some applications, such as in underwater and low-visibility environments, sonar is often the only viable sensing modality.

Sonars in robotics have three different, but related, purposes:

(a) Obstacle avoidance: The first detected echo is assumed to measure the range to the closest object. Robots use this information to plan paths around obstacles and to prevent collisions.
(b) Sonar Mapping: Sonar mapping: A collection of echoes acquired by performing a rotational scan or from a sonar array, are used to construct a map of the environment. Similar to a radar display, a range dot is placed at the detected range along the probing pulse direction.
(c) Object recognition: A sequence of echoes or sonar maps are processed to classify echo producing structures composed of one or more physical objects. When successful, this information is useful for robot registration or landmark navigation.
Some of the famous companies which manufacture sonar sensors are Parallax and Maxbotix. Maxbotix provides a range of 60 sensors along 12 product lines which vary based on the environment, precision, beam width and connection module.

One of the most sought of series is the LV series because of its high precision, robustness, programming simplicity and ease in connection. Various libraries are available for Arduino and other development boards. The only drawback of this series is the resolution (1 inch) which cannot be used where high accuracy is required.

The HR series is the series which gives the highest resolution. They can be connected via USB or direct connection and can be used in indoor as well as outdoor environment. The Maxsonar sensors give both digital and analog reading and can be easily read and converted to distance using some basic formulae. The Maxsonar sensors can also be used for people detection and height detection. One of the most important advantages of Maxbotix sensors is that they can be daisy chained. Daisy chaining is a technique to connect one or more devices together and avoid interference between them. The Maxsonar Sensors can be daisy chained in 3 different ways – the free run mode, the commanded loop mode(software triggered) and the continuous loop mode(hardware triggered).

The sonars belonging to the LV Series have 7 pins and can give both analog and digital output. They can operate at 3.3V and 5V. They also have a pin for series chaining.

(a) Analog Output
The analog output from the LV Sonar can be obatined from the AN pin of the Sonar. The voltage
output is from 0 to Vcc/2 . The resolution of the sonar is 512. This resolution should be taken care of when taking the sonar readings on a microcontroller having a differnet resolution.

(b) Digital Output
The Digital Output can be measured from the PW pin of the Sonar. Whenever the Sonar starts ranging, the PW pin pulled HIGH. Whenever a target is detected, the PW pin is pulled low. The time for which the PW pin is high can be calculated using the pulseIn() function on an Arduino and the distance to the obstacle can be calculated.
(c) Daisy Chaining:
For low noise chaining the BW pin of the sonar has to be pulled high. The chaining can be three
types:

The free run mode, where multiple sonars are ranging continously. This method is to be avoided because it can cause interference between multiple sound waves and give false results.

The chain can be controlled by software using a software controlled loop. The RX of the first sonar is connected to a digital output pin on the microcontroller. The TX of nth sonar is connected to RX of (n+1)th sonar and the RX of first sonar is trigered by atleast a 20us long pulse for all sonars to range once. For every cycle, the RX has to triggered to take the readings from the sonars

The hardware controlled loop is similar to the software controlled loop. The only difference is that the TX of the last sonar is conencted to the RX of the first sonar by a 1K resistor and the RX of the first SONAR needs to be triggered only once. The cycle continues till power is supplied and readings can be taken continuously.

The time from which a SONAR is triggered to the time taken for one ranging cycle is 50ms. So the frequency of readings when one sonar is used is 1s/50ms = 20 . This frequency reduces with increase in the number of sonars. So frequency reduces during daisy chaining.

Our usage: we are using this sonar because it gives a digital output which I can use directly without doing any complicated computations. We can know the distance of the nearest object. By setting optimum threshold values we will know if the objects are obstacles or not.